## Slide 1: Oasys PRIMER: Seat and Dummy Positioning and Belt Fitting
Training course

## Slide 2: Course objective & contents
Objective:
Learn how to use Primer 9.3 to position seats and dummy models, and fit seatbelts.
Course Contents:
Defining the mechanism data for seats
Methods of positioning seats
Storing and retrieving seat positions
Methods of positioning dummies
Storing and retrieving dummy positions
Linking the seat to the dummy for combined positioning
Batch mode commands
Belt re-fitting after dummy positioning
Seat foam compression – Primer method
Seat foam compression – DYNA method
Belt fitting

## Slide 3: Model to be used
We will use a very crude public-domain model during this course, but the same principles can be applied to “real” models.

## Slide 4: Seat positioning

## Slide 5: Mechanism definition
The seat will be positioned by using Primer to define a mechanism, which we can then articulate into the desired position.
Assemblies identified by Parts or Part Sets, e.g. back, squab, front links, etc. During positioning, each assembly will behave as if rigid.
Connections (joints) defined at nodes. These are used purely for positioning the mechanism and are independent of any LS-DYNA joints. Connection types: pin, hinge, sliding.
Reference Points (e.g. H-Point) – mechanism can be positioned by specifying coordinates of reference points.
Assembly
Hinge joint
Assembly
Sliding joint

## Slide 6: Seat – model requirements
Requirements for the Seat model:
  You need to know which parts will be in which assemblies – it is convenient to group these into sets before starting to define the mechanism.
  Nodes must not be shared between assemblies.
  Assemblies should not contain parts that have elements bridging across to other assemblies – that would lead to the “shared node” problem.
  The “joints” in the Primer mechanism are independent of any LS-DYNA connections between the parts. The seat model does not need to contain LS-DYNA joints. Consider instead how you want the model to behave when you run it in LS-DYNA – probably, the mechanism should not articulate, therefore the parts will be fixed rigidly together e.g. using *CONSTRAINED_RIGID_BODIES.

## Slide 7: Workshop – defining a mechanism
Read the model seat_incomplete.key, which contains an almost-complete mechanism definition.
Tools=>Mechanism=>Modify
  (If the model did not already contain a mechanism definition, you would press Create instead of Modify)
This menu allows creation, editing and deletion of Assemblies, Connections, and Reference Points

## Slide 8: Workshop – defining a mechanism
Sketch the mechanism, rotate the model around. The front links, and their connections to the sliding rails and seat frame, need to be added.

## Slide 9: Creating an assembly
Assemblies=>Create; give the title “Front links”; under Parts, drop-down to “pick” and pick the red part. Press “Create_Assy”
In a “real” seat model, there will probably be several parts in each assembly. They can be picked individually, or via a Part Set.
Node sets are available for adding loose nodes to the assembly. This can also be used for elements such as spotwelds whose Part Ids are used in more than one assembly.

## Slide 10: Creating connections
Nodes for connection to sliding rails
Connections=>Create; give title “front links to sliding rails”, choose type=Hinge; For Assembly 1, drop-down to Select, choose the assembly named Sliding Rails; for Assembly 2 select Front Links; pick nodes as shown below; Press “CREATE_MCON”
Create another hinge connection between Front Links and Seat Base
Nodes for connection to seat base

## Slide 11: Adding a Reference Point
Mechanisms can have any number of reference points. Each may be positioned to user-specified coordinates.
Create a point named “H-point”. Switch the definition method to “node”, and pick the node at the apex of the triangle that sticks out through the seat cushion.
Attach the reference point to the Seat Base assembly.
Press CREATE_MPNT
To save all the changes to the mechanism definition, press “UPDATE_MECH”

## Slide 12: Using the Drag Assemblies menu
Press Position. Primer starts in the “drag assemblies” sub-menu: this allows the assemblies to be restrained. (You can still drag the mechanism in any of the four sub-menus within the Position menu).
In the model provided, the “fixed rails” have been restrained.
Try dragging the seat cushion – set the view roughly side-on.
Try removing the restraints from the fixed rails; drag again.
Press “Reject”. This returns the mechanism to the configuration it was in when you entered the Position menu (or when you last pressed “Accept”).
Go back into the Position menu, and put back the restraints on the fixed rails. Try restraining the sliding rails, then drag the cushion. Release the sliding rails again.

## Slide 13: Using the Connection List menu
Go to the Connection List sub-menu
In the model provided, the seat back hinge and the headrest slider are locked.
Experiment with releasing these, then dragging the seat back or headrest.
Try locking other joints to see the effect.
Remember, you can always press “Reject” if you don’t like the result.
The positioning has no permanent effect until you press “Accept”.

## Slide 14: Using the Rotate Angles menu
In the Connections menu, check that the seat back hinge is released.
Restrain the seat base (in the Drag Assembly menu)
Go to the Rotate Angles menu.
Drag the seat back and note the Y-axis angle changing
Type an angle into the y-axis angle box for the seat back and see the effect.
Angles are defined as the orientation of the assembly in the global axis system, relative to its orientation at the time the mechanism was created.
Reject this position and go back into the Position menu.

## Slide 15: Using the Position Points menu
Now reset the restraints (in the Drag Assemblies menu) – only the fixed rails should be restrained; and in the Connections menu, only the seat back hinge and headrest slider should be locked.
Go to the Position Points menu.
Type in H-point coordinates 500 * 175 (* means “don’t care”)

## Slide 16: Saving and retrieving positions
Save this as a New Position, calling it “Rear Low”, then press “Save It” and Done.
Type in H-point coordinates 350 * 250. The H-point cannot reach this position – it is outside the possible locus with this mechanism. Note the message in the dialog box telling you that there is a “Delta” (difference between what you asked for and what Primer could achieve).
Save this position, calling it “Front High”.
Now retrieve the position “Rear Low”, and swap back to “Front High”.

## Slide 17: How the mechanism data is stored
Finally, return the seat to the base position (the first stored position), and write out as a new keyword file seat_positioned.key.
Using a text editor, look at the end of the keyword file (after *END). The keywords between *MECHANISM_START and *MECHANISM_END contain the mechanism data and stored positions. These will be available in Primer next time this model is read in.
Delete the seat model from Primer, ready for the next exercise.

## Slide 18: Dummy positioning

## Slide 19: Workshop - dummy positioning
Read dummypos_start2.key.
The dummy is in its “neutral” position.
The dummy’s tree file is automatically used by Primer to allow the dummy to be positioned like a mechanism – you do not have to create the mechanism data.
Go to Occupant=>Dummies=>Position

## Slide 20: Workshop - dummy positioning
“Set H-point”, type in the coordinates 420 200 215
“Rotate”, for the centre of rotation choose “use H-point”, type in angles 0 23 0, Apply.

## Slide 21: Dummy positioning – Rotate Angles
“Move Parts” brings up a menu very similar to the Mechanism Positioning menu.
The initial sub-menu is Rotate Angles, which is the dummy positioning capability from Primer 9.2.
In this menu, dragging is by left, middle and right mouse buttons for rotations about the local X, Y and Z axes (Phi, Theta, Psi in the menu). Green colour indicates a degree of freedom that can be dragged.
You can also type the desired angles in the menu.
Use the middle mouse button to drag the left lower leg to a new position.

## Slide 22: Dummy positioning – Drag Assembly
Change to the “Drag Assembly” submenu. The Torso, hands and feet have already been restrained.
Check the restraints on the torso – it should be fully restrained while we position the limbs.
Cancel the translational restraints from the left foot. Drag the foot onto the footrest.
Also try restraining the rotations (but not translations) of the foot, then dragging it into position. This technique is useful for putting feet and hands into roughly the correct position.
If you want to start again, press Reject and go back to the Position menu.
X-translation
Y-translation
Z-translation
X-rotation
Y-rotation
Z-rotation

## Slide 23: Dummy positioning – Drag Assembly
Explanation of mouse actions in this sub-menu:
  In this menu, left mouse is normal dragging
  Middle mouse button is for dragging with the next assembly down the tree temporarily locked (e.g. if you drag the foot like this, the lower leg will be locked).
  Right mouse allows freedom the dragged assembly and its immediate neighbour; this is useful with dummy models that have small assemblies in the wrists and elbows.
Try the effect of dragging the foot with the middle mouse button, then the right mouse button.
Complete the positioning of left foot onto footrest

## Slide 24: Dummy positioning
Drag the right foot to rest on the floor
Drag the left and right hands onto the steering wheel.
To make the right hand exactly match the left, go to the Rotate Angles submenu, observe the angle of the Left Yoke, and type in the same angle for the right yoke. Depending which way around the joint is defined, the angles for left and right may have opposite signs.
Make the angles match also for the right upper arm, right lower arm, right hand.

## Slide 25: Saving dummy position
Press Accept
Primer will find that some nodal pairs at joints are no longer exactly coincident. Check the nodal separation; if small, select AUTOFIX to make the joint nodes coincident. This results in slight geometry change to the model.

## Slide 26: Dummy positioning
We will now hold the hands and feet fixed, and move the H-point.
Apply translational and rotational restraints to the hands and feet.
Free the X and Z translational restraints on the Torso.
Try dragging the torso to a new position.

## Slide 27: Dummy positioning – Move Points
Go to the Move Points submenu
This works in the same way as the Mechanism menu
Type in new coordinates for the H-point: (320 * 280)
Save this position as “Front High”
Now type in H-point “delta” (100 * -80)
Save this position as “Rear Low”
Retrieve Front High and Rear Low alternately.

## Slide 28: Dummy angles file
In the Save/Retrieve menu, write a Dummy Angles file (test.daf)
Look at the file in a text editor
The saved positions are intended to be used within the same model. The dummy angles file can be read in to different models, provided that the dummy model has the same assemblies and joints.

## Slide 29: Workshop – linked seat/dummy
Delete any existing models from Primer
Read in dummy_seat_ready_for_linking3.key
We will link the dummy as a “slave” to the seat. Then, if we move the seat, the dummy will also move, but not vice-versa.
Go to Tools=>Mechanism=>Modify
Children=>Create

## Slide 30: Workshop – linked seat/dummy
Under Assembly, select the Seat Base.
Under Dummy, select the only dummy
Select the Torso to be linked
Linked degrees of freedom: select X Y and Z
Press CREATE_MMCH
Press UPDATE_MECH to save the changes in the model

## Slide 31: Workshop – linked seat/dummy
Now go to Mechanism=>Position, Drag Assemblies, check that the restraints are correct (hands/feet fixed, torso free in X and Z; fixed rails restrained).
Try dragging the seat base. Reject.
Now go to Mechanism=>Position, Position Points sub-menu
Type in new H-point 320 * 180
Save position as “seat-dummy front low”
Type in H-point delta = 100 * 0
Save position as “seat-dummy rear low”
Retrieve “seat-dummy front low” ready for the next workshop.

## Slide 32: Mechanisms/Dummies – Command File
Mechanisms and dummies may now be positioned using command-line (for example, in a command file as part of a batch process). Example:
/READ DK seat_model.key
/MECHANISM
ASSEMBLY 6
FIX 123456
DONE
POINT H-Point
POSITION 1250 400 350
DONE
ACCEPT
/WRITE DK new_model1.key
/MECH
POINT H-Point
POSITION 1350 400 380
DONE
ACCEPT
/WRITE DK new_model2.key
New command MECHANISM
Can restrain, translate or rotate assemblies. If the correct restraints were already saved in the keyword file, there is no need to add commands here to restrain the assemblies.
Can restrain, translate or type new coordinates for (“Position”) Reference Points.
This command file writes two models, each with the H-point in a different position.

## Slide 33: Mechanisms/Dummies – Command File
To find the available commands, type “H” (for “Help”) in the dialog box. Type one of the options shown in the menu. Type “H” again… etc.
The same commands that can be typed in the dialog box, will also work when used in a command file.

## Slide 34: Belt re-fit
Works only if belt was initially fitted in Primer, version 9.3 and upwards.

## Slide 35: Belt re-fit
After repositioning dummy and seat…
… Use Seatbelt=>Auto-refit
Try this using your model in “front low” position, then “seat-dummy base”

## Slide 36: Belt re-fit
Belt automatically re-fitted and remeshed
Primer uses the same meshing parameters and element types as the initial belt mesh

## Slide 37: Seat foam compression

## Slide 38: Seat foam compression
Dummy has been positioned, penetrating the foam
User invokes Seat Squash feature, selects the dummy/seat contact and the top and bottom surfaces of the foam.
Primer raises dummy until there are no penetrations.
“Primer Method”: Primer pushes the dummy back down, compressing the foam evenly to prevent penetrations.
“DYNA Method”: Primer helps the user to create an LS-DYNA model in which a rigid dummy will be pushed into the seat, and then import the deformed seat node coordinates into the model.

## Slide 39: Seat foam compression methods
Model with compressed seat foam
PRIMER prepares model for LS-DYNA analysis
LS-DYNA analysis
“dynain” file
PRIMER lifts dummy out of seat
PRIMER lifts dummy out of seat
Model with dummy penetrating seat
PRIMER takes foam coords (and initial stress if required) from dynain file
“PRIMER method”
“DYNA method”
PRIMER pushes dummy back into seat:
Top surface of seat de-penetrated as dummy moves
Interior foam nodes positioned using geometric algorithm to spread strain evenly

## Slide 40: Seat foam compression – LS-DYNA analysis
Fully rigid dummy with BOUNDARY_PRESCRIBED_MOTION to return it to original H-point

## Slide 41: Seat foam compression – LS-DYNA analysis

## Slide 42: Seat foam compression – LS-DYNA analysis
New coordinates of foam nodes written to dynain file

## Slide 43: Oasys PRIMER method versus LS-DYNA method
Result is a more realistic deformation of the seat
Other parts can deform, not only the foam
Can include initial stresses if required
Time taken: 5-30 minutes including LS-DYNA analysis
Result is an imprint of the dummy shape into the foam
Only the foam is deformed
No initial stresses
Time taken: 1-5 minutes
Oasys PRIMER method
LS-DYNA method

## Slide 44: Workshop – seat foam compression
If you do not have the seat/dummy model already in Primer, read dummy_seat_ready_for_linking3.key
The H-point of both dummy and seat should already be at (420, 200, 215)
The dummy is penetrating the foam. In this workshop we will try both Primer and LS-DYNA methods of seat foam compression.
First, we will set up a view that shows the interior elements of the foam under the dummy.

## Slide 45: Set up a cut section
Shortcut X brings up the cut section menu
Shortcut N then allows you to pick a node where the section should be cut – pick a node on the dummy’s left leg
Change definition method to “Constant Y”
Change Positive Action to “normal”
Shortcut D then drag the section through the model, until at the thickest part of the left leg.
Shortcut Q returns the mouse action to normal (Quickpick)

## Slide 46: Add mesh overlay
View the mesh: bring up the Display Options menu (shortcut O)
Set “All edges” (or use shortcut Y)
For extra clarity, set the overlay colour to black

## Slide 47: Export the initial foam geometry
Go to Tools=>Occupant=>Seatsquash
It is useful to keep the initial coordinates of the foam nodes – these can be imported into the model later if required.
Use the Export button, selecting Part 8 (the foam), and giving file name seat_foam_undeformed.k

## Slide 48: Oasys PRIMER-method foam compression
Select Squash, then Primer method
At each step, instructions appear.
Foam = Part 8
Top surface of seat = Part 10
  The nodes belonging to this part will be depenetrated using the contact definition below
Bottom surface of foam = Part 11
  The nodes belonging to this part will remain fixed
Dummy = (select the only dummy)
Contact = (select the first contact)
Instructions are given here

## Slide 49: Oasys PRIMER-method foam compression
X, Y and Z increments = displacement of dummy per iteration.
  Dummy is first moved in positive vector direction until there are no penetrations.
  Then the dummy is moved in the negative vector direction until either the original H-point is reached, or else the elements become too distorted.
Enter a Z increment 1.0, leave X and Y zero.
Reduce the relative volume check to 0.1
  The elements in this model are large, so a lower limit is OK. With typical real models meshed with tetrahedra, leave the default 0.2.
Press Next and Apply – Primer moves the dummy up out of the seat, then down compressing the foam.

## Slide 50: Oasys PRIMER-method foam compression
The result should be as shown.
Export the new coordinates (part 8) using filename seat_foam_primer.k.
Depending on the requested dummy position and the degree of deformation imposed on the foam, Primer may fail to achieve the required position. Check the dialog box for any error message.

## Slide 51: Oasys PRIMER-method foam compression
Model requirements for Primer method foam compression
  Foam coated with shells (can be *MAT_NULL or fabric, leather, etc) – to create these elements use Tools=>Coat. This will generate shells on all exterior surfaces of the foam.
  The shell element coating needs to be split into parts for the “top” and “bottom” surfaces. “Top” surface should cover anywhere that the dummy might contact. See parts 10 and 11 in this example.
  Contact between dummy and seat. The contact thickness must be at least twice the selected step size. In this example model, the contact thickness was set to 2.0mm, the step size was 1.0mm.
Foam solid elements can be any type (hexa, tetra, wedge). Failure to compress the foam to the desired H-point may be due to poorly meshed tetrahedron elements, especially where these are initially almost flat. Such elements may also lead to “negative volume” problems in LS-DYNA. Primer includes a mesh-improvement step to help with this (for tetrahedra only).

## Slide 52: LS-DYNA-method foam compression
We will now try the DYNA method of foam compression
Either delete the model from Primer and re-read, or import the foam coordinates from seat_foam_undeformed.k
For the purpose of creating an LS-DYNA seat foam compression analysis, we do not need the steering wheel or floor. Remove them using Tools=>INCLUDE=>(drop-down from footrest+floor.k to EMPTY INCLUDE), with option DELETE_2 and agree to delete the Include file. Similarly, remove strg_wheel.k.
  In real models, there may be many other parts to delete, such that you are left with just the seat and dummy.

## Slide 53: LS-DYNA-method foam compression
Deformable parts = Part 8
  With more complex seat models, we may also wish to leave other parts deformable, e.g. the springs or membrane supporting the foam
Dummy = select the only dummy
Do not select any parts of the dummy to remain deformable.
Contact = select the first contact
Internal contacts to remove – accept Primer’s suggestion.
  In some models, internal contacts within the seat may need to be kept to prevent penetration of the deformable parts of the seat
Go to Seatsquash=>Squash and select DYNA method.
For the seat, select INCLUDE file seat_complete.key

## Slide 54: LS-DYNA-method foam compression
X, Y and Z increments = 0, 0, 1. The step size is less critical with the DYNA method – if too large, there will be more initial gap between dummy and seat.
Enter 0.02 for “time to position dummy”
Enter 0.025 for “Total analysis time”
Leave the damping input as per Primer’s default
Press Next and Apply
0.02 0.025
time
displacement

## Slide 55: LS-DYNA-method foam compression
If warnings appear about PART_INERTIA losing mass, press OK
The dummy will now rise out of the seat; lines will appear as Primer rigidifies the dummy and the non-deformable parts of the seat.
The model should look like this:

## Slide 56: LS-DYNA-method foam compression
Go to Keyword=>BOUNDARY=> PRESCRIBED_MOTION =>Keyword. You will see the motion definition that Primer has created, to move the dummy back to its initial position during the LS-DYNA analysis.
Motion in Z-direction

## Slide 57: LS-DYNA-method foam compression
The model includes *INTERFACE_SPRINGBACK_LSDYNA. Primer has created this card to force LS-DYNA to write a keyword-format file (“dynain”) at the end of the analysis, from which the foam coordinates and stresses can be taken.
Write out the model with filename “foam_compress.key”. For simplicity, merge the INCLUDE files into the master model (option during model write-out).

## Slide 58: LS-DYNA-method foam compression
Run the model in LS-DYNA – it should take about 10-30 seconds.
Check that LS-DYNA has written a file named dynain. Look at its contents with a text editor.
  *NODE cards will be used to modify the coordinates of the foam nodes
  *ELEMENT cards will be ignored
  *INITIAL_STRESS cards can optionally be read in to prestress the foam
Animate the results in your usual postprocessor. It should look like this:

## Slide 59: LS-DYNA-method foam compression
In Primer, delete all existing models. Read in dummy_seat_ready_for_linking3.key
Occupant=>Seatsquash=>Import, select the dynain file.
Import all parts in the file (it will be only the foam).
Switch off INITIAL_STRESS cards – to use these effectively, the new model would need gravity, so that the weight of the dummy would have to be in equilibrium with the foam stresses. But this introduces complications such as the dummy slumping out of the intended position.
The model should now look like this:

## Slide 60: Foam compression – other notes
Sometimes, the Oasys PRIMER-method foam compression algorithm may fail to reach the final end-point. This is usually due to sharp edges on the dummy, e.g. the bottom edge of the jacket, or leg-to-pelvis gap.
We would generally recommend the LS-DYNA method to obtain the most accurate results when the initial penetration is large.
For small adjustments to the dummy position, the Primer method is usually adequate.

## Slide 61: Seatbelt fitting

## Slide 62: Seatbelt fitting – first steps
We have already seen how to re-fit an existing seatbelt. Now we will learn how to create and fit a new seatbelt.
Delete existing models from Primer.
Read dummy_seat_for_belt_fit.key.
Before we start work, consider into which Include File we want the new belt elements to be placed. Set this Include file as the “current layer”.
Go to Tools=>Occupant=>Seatbelts.
In the seatbelts menu, press “1. Define”, then “Create”, and “Apply”.
We now select the parts that can be contacted by the belt during fitting. In the object menu, select the object type “Part”, then click on the chest and pelvis of the dummy. Press “Apply”.

## Slide 63: Seatbelt fitting – path definition
Press “2. Fit”.
Press the “Dimens” button and set the length of the belt elements to 15mm, and the #rows to 4 (4 elements across the width of the belt). Press “Done”.
Press “Define path”.
We are now going to pick nodes forming the path of the belt, starting at the retractor. To make it easier to see the nodes, use shortcut Y to add the mesh overlay.
Try to pick nodes approximately as shown on the next slide.

## Slide 64: Seatbelt fitting – path definition
1. For retractor – on B-post
2. For slipring – on B-post
3. On dummy’s chest
4. On dummy’s chest
5. On buckle block
6. On dummy’s pelvis
7. On dummy’s pelvis
8. For fixed end – on B-post

## Slide 65: Seatbelt fitting – path definition
Change point 1 to be a retractor.
Change points 2 and 5 to be sliprings.
Check that the prototype mesh does not penetrate through the chest or pelvis of the dummy. If it does, move the path points (press “Modify coords”, then left, middle and right mouse buttons for X, Y and Z directions).
It is also possible to control the twist of the belt path if you wish (“Control twist”, then use the drag handles).
When you are satisfied, press “Save”.

## Slide 66: Seatbelt fitting – fitting
Press “Fit”. Primer tightens the prototype belt mesh onto the dummy.
If the result looks reasonable, press “Accept”. If not, go back to “Define path” and modify the initial path, then Fit again.

## Slide 67: Seatbelt fitting - meshing
Next we will mesh the belt. The prototype mesh seen in the previous steps exists only to show where the mesh will be created.
Press “3. Mesh”.
Primer now displays the first “segment” of the belt, from retractor to slipring.
We will choose to use LS-DYNA’s 1-dimensional *ELEMENT_SEATBELT. The “meshing type” radio button is already set to “Sblt 1D only” – this is they type we want.
To select a part for the new seatbelt elements, press “1D Sblt props” and right-click on the Part ID, Select, scroll the list of parts to the end, select part 1000002. Press “Update property”.

## Slide 68: Seatbelt fitting - meshing
Press the button marked “[>]” to display the next segment of belt (across the chest).
This time we want a mixed mesh, with 1D elements near the sliprings (so they can pass through the sliprings) and shell elements elsewhere to provide a realistic contact condition to the dummy.
This is already the default (“Mix Sb1/Shl”). Also, we can leave the default number (4) of 1D elements at each end.
To select a part for the new shell elements, press “Shell props”, right-click on the Part ID, Select, scroll down the list, pick part 1000003. Press “Update property”.
Move to the final belt segment using “[>]”. Check that the settings are correct.
Press “Generate”, press OK.

## Slide 69: Seatbelt fitting – error check
The next menu highlights (in red) any error found.
Click on “1D SB Matl”. Press “Check defn”. Primer will explain the error. Press “Continue”.
  Change LMIN to 5(mm)
  Press “Update”.
Click on the red “Retractor” button, and “check defn”.
  Select the only sensor for SID1.
  For LLCID, select curve 1000004
  For ULCID, select curve 1000005
  Update Element.
Also click on the slipring button. For each slipring, change the friction (FC) to 0.2.

## Slide 70: Seatbelt fitting – define contact & save model
Press “4. Contact”.
We will create a surface-to-surface contact for the belt to the dummy.
Under “AUTOMATIC_SURFACE_TO_SURFACE”, press “Create”
Now write out the model under a new name.

## Slide 71: Summary
We have covered the following subjects using a simplified model:
  Defining the mechanism data for seats
  Methods of positioning seats
  Storing and retrieving seat positions
  Methods of positioning dummies
  Storing and retrieving dummy positions
  Linking the seat to the dummy for combined positioning
  Batch mode commands
  Belt re-fitting after dummy positioning
  Seat foam compression – Primer method
  Seat foam compression – DYNA method
  Belt fitting
Have fun with your real seat and dummy models!

## Slide 72: Oasys PRIMER: Seat and Dummy Positioning and Belt Fitting
Training course