## Slide 1: Oasys PRIMER: Spotwelding and Connections
Training course

## Slide 2: Course objective & contents
Objective
Learn how to create, modify and check spotwelds in Primer10
Course Contents
Creating individual spotwelds
Autoweld
Using spotweld files, fixing bad welds
Using the Connections Table
Checking spotwelds
Creating bolts
Using connections files for bolts
Creating connection data from existing FE models
Creating Adhesive

## Slide 3: Creating spotwelds
Read in biw_for_welding.key
Right-mouse-drag across right-hand upper B-post parts, “Only”.
Make these parts 50% transparent (e.g. right-mouse-drag across=>transparency=>50%)
Zoom in on the right-hand upper B-post: we will start by creating spotwelds on the forward flange.
Switch on the element borders (shortcut “Y”)

## Slide 4: Creating spotwelds
Tools=>Connection=>Create
The Connections menu is used for spotwelds and other connection types
First we have to tell Primer which panels can be considered for welding. This model consists only of body panels so we can just select all the shell-element parts in the model.
Press “all”.
Note we could also select only “visible” shells, or explicitly select shells using “Select shells to connect”.

## Slide 5: Creating spotwelds
Leave the spotweld type set to Beam.
This model already contains an empty Part ID for the beam spotwelds (ELFORM=9, *MAT_SPOTWELD). Primer automatically finds this and uses it. If this part were not present in the model, you would have to create one first before creating the spotwelds.
Try the “pick screen point” option.
Click on a point on the forward flange of the lower B-post.
A green spotweld appears.
Rotate the view: Primer found 3 layers to be welded, so it created a chain of 2 beams.
Note: You may need to adjust the spotweld Max Length in the Settings window.

## Slide 6: Creating spotwelds
Switch the element type to Hexa.
Again, a suitable part is already present in the model so Primer uses it.
Click on the flange in several places: a solid spotweld appears in each place.
Also try 4-Hexa.

## Slide 7: Creating spotwelds
Change to Line of Welds.
Change spacing option to Pitch, set a pitch of 40mm.
Switch element type back to Hexa.
Form a segmented line on which the welds will be placed, by clicking points as shown.
Press “sketch weld positions” to see where Primer will put the welds.
Press Apply.

## Slide 8: Autoweld
Switch the creation method to Autoweld. With this option, Primer tries to create welds at a user-defined pitch, using the free edges of the panels as a guide.
This option is used when no information is available about the actual locations of the spotwelds.
Set the “min run length” to 50, i.e. Primer will try to spotweld any flange longer than 50mm.
Check that the weld pitch is 40mm.
Unblank all parts (shortcut “U”)
Press Apply.

## Slide 9: Autoweld
There will be places where Primer has not created welds (e.g. where the panel gaps are too large), so the model still needs to be checked carefully!

## Slide 10: Creating spotwelds
When creating spotwelds, Primer also creates connection entities. These are the green circles. If you wish, visibility of these can be switched off using the Entities panel.
This entity visibility switch will automatically be switched on whenever new spotwelds are created.

## Slide 11: Adding a tied contact
After creating spotwelds, we need to create a tied contact to stick them to the panels.
When you Dismiss the Spotweld Create menu, Primer reminds you to do this.
Press “Contact”, “Create connection contact”.
Click on “Two contacts” in the pop-up.
Primer creates a *CONTACT_TIED_SURFACE_TO_SURFACE for solid elements, or a *CONTACT_SPOTWELD for beam elements
If rigid parts or Nodal Rigid Bodies are present, two tied contacts are created - Primer also creates an _OFFSET (penalty-method) tied contact to stick the spotwelds affected by rigid entities.

## Slide 12: Writing a spotweld file
Dismiss the Spotweld Create menu (e.g. press ESC while the mouse is in that menu).
To save the newly created spotwelds, we should either write out a keyword file, or write a spotweld file. The spotweld file contains the coordinates of each spotweld, and which panels are connected. The same spotwelds could be re-created in another similar model from the spotweld file.
“Primer spotweld file” = simple csv format, one line per weld.
“XML connection file” = xml-format, contains more information e.g. whether the welds are beam or hexa.
Unigraphics (UG) format weld file is also available.
We would recommend to choose a XML Connection file, to avoid losing any information.
Write a connections file named example1.xml.

## Slide 13: Reading a spotweld file
Before reading the spotweld file, we will delete all the existing spotwelds.
Press Delete, leave the selector on “All connections”, Apply.
Click “Delete CONX & FE” in the pop-up.
Press Read, set the file format to “Spotweld File”.
Browse to find the file sptwld.spt
Check that the spotweld element type is set to Hexa
Press Apply

## Slide 14: Reading a spotweld file
An image of the file contents appears
“Primer spotweld file” format can be used for files written by other software – the meaning of each column may be controlled from the drop-down menus. The limitation is that the file must have only one line per spotweld.
Move the menu so you can see the vehicle.
Press Apply.
Drop-down menu to change meaning of column of data

## Slide 15: Reading a spotweld file
Primer creates the spotwelds (green symbols) where possible. Bad welds are shown in red.
A message appears stating how many spotwelds were successfully created, and how many were not. Press Continue.
Most spotweld files contain some errors. Fixing the errors can be a time-consuming task. Primer automatically puts the bad welds into the Connection Table.
We will now use the table to fix some of the errors.

## Slide 16: Using Connection Table to fix bad welds
Try hovering over some of the text in the “error” and “details” columns.
Try sorting the table by clicking on the column headers.
Go back to sorting by ID (left-hand column).
Select the first five welds (click and shift-click), right-click “Show conx and panels”.

## Slide 17: Fixing errors
The selected connections, and the panels referred to, are displayed.
The error is clear – the right-hand A-post has been referenced instead of the left-hand one.
Right-click on the data in Layer 1 (P10000001), drop down to “Select PID”, select part 10000000 (the first part in the list).

## Slide 18: Fixing errors
The revised data is shown in red.
To update the connection data and remake the weld, right-click and “update & remake”
Again, request “show conx and panels”. Check that the correct panels are now shown.
Do not worry about the “NOT CONNECTED” error that now appears – this is because we have not yet created the tied contact.

## Slide 19: Fixing errors
Click on weld 71, “show conx and panels”.
Primer could not create a hexa weld, because the element would have been warped. The position of the connection is too near a fold-line, it needs to be moved.
To do this, use “View” to add columns for X Y and Z.
Right-click on the X-coordinate, “Pick (from shell)”

## Slide 20: Fixing errors
Adjust the view so you can see the flanges clearly.
Click on a new position nearer the middle of the flange and further from the edge of the green panel.
The new position appears as a black dot.
Right click and “Update & remake”
Old position
New position

## Slide 21: Fixing errors
Scroll through the remaining welds. Weld ID 1139 to 1142 reference non-existent panel PIDs. Use the action “delete connection” to remove these:
  Change action at top of menu to “delete connection”
  Next to “All”, press “Selected”.
  Chose “Delete FE”
We could continue to fix the bad welds using these methods.
Dismiss the table.
Use the Connections=>Contact tool to create the tied contact.
Write a connections file and/or a keyword file to save the corrected data.

## Slide 22: Reprojecting welds
If the panel geometry is modified, the spotweld elements may no longer be coincident with the panel element planes. The spotwelds need to be reprojected.
To do this, you would select the spotwelds attached to the modified panel to be opened in the Table, Select all welds in the table, update & remake. (Do not do this now)
Select panel or screen-pick

## Slide 23: Other uses of the connections table
The table can be used to check or modify a subset of the spotwelds, e.g. those connected to a particular panel.
Set the selector option to “by attached panels”, press VIS, and pick the blue underfloor longitudinal.
Press Apply

## Slide 24: Other uses of Connection Table
Primer puts only those welds connected to the selected panel into the table.
By setting the action to “show connection and panels”, selecting all the welds in the table, and pressing “apply selected”, you can check for missing welds.

## Slide 25: Changing spotweld type
We will now change the type of elements used for these spotwelds.
Using View, add Type and Subtype. Un-check the columns for X, Y and Z.
Leave all the welds in the table selected.
Right-click on the column for subtype, choose 4 solids, and update & remake the spotwelds. Inspect the welds created.
This method can also be used to change between beam and solid element spotwelds, provided that the model already contains a suitable Part ID.

## Slide 26: Connection Table
Sometimes it is advantageous to describe the layers that connect to each spotweld in a more general way than Part ID. For example, a taylor-welded blank may consist of several parts. The Table permits description of layers by a list of parts, by part set, etc.

## Slide 27: Checking spotwelds
Various tools are provided for checking spotwelds.
“Find Con(nected)” means “show welds and panels”. This allows you to check visually for missing welds.
Set the selection method to “welds/bolts/adhesive from attached panels”
Pick the first part in the list, press Apply.
Primer shows all the welds and panels connected to the selected panel.

## Slide 28: Checking spotwelds
Switch to “weld seams from panels”.
Select parts 10000006 10000008 and 10000010.
Press Apply.
This option displays only the selected panels, and any welds that connect any combination of those panels, e.g. 10000006 to10000008.

## Slide 29: Checking spotwelds
Switch to “single seam from panels”.
Select the same parts, Apply.
This option displays only spotwelds that connect between all of the selected panels.

## Slide 30: Checking spotwelds
Press Find unc(onnected)”
Primer displays any parts not connected by at least one spotweld

## Slide 31: Checking spotwelds
Press Check
“Conflicting” – are any pairs of spotwelds too close to each other? Try distance = 20mm. First try “List”, then try “Table”.
The other two options, “Connectivity” and “Contact”, are now superceded by the main “Contact” menu.
Try also the Connections=>Contact menu. This is for checking and correcting the tied contact.
Try changing the material of one of the body panels to rigid, re-check the tied contact.
Now, some of the spotwelds do not tie, due to constraint clash with constraint-type tied contact. Use the Sketch Conx => untied to view them
Re-make the tied contact.

## Slide 32: Connection entities
Each spotweld has a corresponding “connection entity”, which stores the instructions for making the connection.
This method has several advantages:
  Failed welds are retained in the model, can be fixed any time.
  When creating from a spotweld file, the original XYZ coords are retained.
  Easy to change the welds, e.g. beam-to-solid.
Other connection types are possible: bolts, adhesive.
Weld file
Spotwelds
LS-DYNA model
Primer 9.3:
Bolts, etc
Connections

## Slide 33: Connection entities
Connection entities are written to the keyword file after *END:
The associated FE entities are referenced, so that Primer knows which to delete if the connection is deleted or remade.
If the model contains spotwelds but not connection entities (e.g. if the spotwelds were not made by Primer), these will be created automatically on entering the Connections menu.
*CONNECTION_START_SPOTWELD
-291.77676 497.33395 346.71783 0 5.0 9998 2
*CONNECTION_LAYER_PART_ID
10000066
*CONNECTION_LAYER_PART_ID
10000051
*CONNECTION_ENTITIES
NODE 10277709 10277710 10277711 10277712 10277713
NODE 10277714 10277715 10277716
SOLID 10001723
*CONNECTION_END_SPOTWELD

## Slide 34: Connection entities
The disadvantage of having Connections entities is that confusion can arise if the connection entities become separated from their associated FE data, e.g. if split across INCLUDE files and only one of the files is read in.
By default, Primer creates new connection data and the associated FE entities in the “Current Layer”.
There are options in the Connections Table to manage the Include File location of connection data.

## Slide 35: Bolt connections
As well as spotwelds, Primer offers a “bolt” connection type.
Bolts can be “realized” as rigid patches or nodal rigid bodies
Notes: <number>
For example, bolts may be represented by nodal rigid bodies, or by rigid patches connected by *CONSTRAINED_RIGID_BODIES. Because of the stored connection data, Primer can delete one type of bolt connection and make a different type.
The connection data (including bolts, spotwelds, and others) can be written to and read from a “connections file”.

## Slide 36: Bolt connections
Manual creation of bolts through Tools=>Connections=>Create
This is very similar to creation of spotwelds
Bolt selection button

## Slide 37: Bolt connections
Manual creation of bolts through Tools=>Connections=>Create:
  Selection of shells/parts to connect.
  Bolt creation method:
    X, Y, Z coords – type in coordinate of bolt.
    Screen point – click on the screen to create bolt.
    Single node – pick an existing node as the position of the bolt.
    Edge of hole – pick a node at the edge of a hole and Primer will calculate the centre of the hole to use as the bolt position.
    Between nodes– pick two or more existing
    nodes, the bolt is created between them. Useful for creating bolts over holes.
    Pick connection – pick an existing Primer connection point.

## Slide 38: Workshop – creating bolts
Read in model demo_bolts2.key.
Blank all parts, unblank parts 260, 264, 276.
Select the shell elements to connect (the unblanked parts – use “visible” button).
Selection method “screen point”
Set diameter to 15mm
Create a “Cylindrical merge” bolt at the locations shown.

## Slide 39: Workshop – creating bolts
Undo_create (this removes the last one), change diameter to 20mm, and select the point again.
Change bolt type to NRB (Nodal Rigid Body)
Undo_create, and select the point again.

## Slide 40: Bolts from connection file
Next we will try creating bolts from a connection file.
Delete all the connections in the model.
Read connections file bolts2.xml

## Slide 41: Bolts from connection file
The results should look like this:

## Slide 42: Bolts – connection table
The Connection Table can be used to modify bolts, in the same way as for spotwelds.
You could even change a connection from a bolt to a spotweld or vice-versa.
Start the connection table, asking for all connections in the model.

## Slide 43: Bolts – connection table
Try changing the diameter of the first 15 nodal rigid bodies to 40mm; update & remake; Apply selected.

## Slide 44: Bolts – creating connection data
If the model already contains bolts modelled by NRB or merged rigid patches, but does not contain connection entities, you will not be able to remake the connections, write them to file, apply in another model, etc.
Using the “From FE” feature, Primer can find bolts in the model by matching rigid body merges or nodal rigid bodies against the user-supplied size and part list.

## Slide 45: Bolts – creating connection data
Automatic creation of connection points from FE data (note as well as rigid constraints beams and adhesive solids and be converted here as well):
  Various options are available when creating connection points from FE data:
The maximum size of the constraint selected can be set here
The type of FE selected can be chosen here
For “Selection mode”, if “FE item” is chosen a list of all the rigid constraints of the selected type (NRB or merge) appears at the bottom. You select the constraint(s) you wish to convert to a connection definition here

## Slide 46: Bolts – creating connection data
Delete all models from Primer.
Read model bolts_without_connx2.key
In the entities panel (shortcut key ‘e’), switch on Constrained.
View the model – the bolts are present.
Go to the Connection menu. Most of the buttons are greyed out, because no connection data is present.
Press From FE
Set the FE item to “all nrbs”, switch selection mode to “attached to part”. Select ALL parts (in this case Primer will look for NRBs attached to all parts in the model)
Enter 40 as the maximum size (NRBs larger than this will be assumed not to be bolts); Press Apply
Check in the Connection Table that connections have been generated.
A connections file could now be written, allowing the same bolts to be re-created in another model.

## Slide 47: Bolt Connections Summary
1 point
Cylindrical
patch
1 point
Spherical
NRB
1 point
Cylindrical
NRB
2 point
Cylindrical
Full connection
Deformable beam
Spherical joint
Discrete beam
Revolute joint
Rigid beam
Deformable beam + NRB
Deformable beam + patch
Zero length entities (spherical joint & discrete beam) are created at the geometric mid-point between layers for cylindrical geometries…
… and at the CONX position for spherical geometries

## Slide 48: Adhesive – create manually
Delete model from Primer. Read joint_bpost.key.
Blank all parts except 8712, 82151.
Connection=>Create=>Adhesive.
Select the visible parts (“visible”)
Select part 9997.
Width = 12mm
No of solids across = 2
Element length = 6mm
Create a line on the left-hand flange, Apply.
Don’t close the window
Use a Line plot to view the result (shortcut “L”).

## Slide 49: Adhesive – create manually
Click “Undo create” to delete the adhesive just created.
Switch the creation method to “free edge”.
This allows you to create a run of adhesive from one free edge. Select 2 nodes along one free edge to create the adhesive.
Two nodes picked along part free edge

## Slide 50: Adhesive – automatic creation
Click “Undo create” to delete the adhesive just created.
Change to auto-adhesive method. This method uses the panel free edges to decide where to create the adhesive.
Sketch adhesive, check the result. At the corners, some elements have overlapped.
For “master part”, select the green part. Sketch again. Now, only the green part’s free edge is used to decide where to create the adhesive.
Apply.

## Slide 51: Adhesive – modifying the path
Dismiss the adhesive creation menu.
Create a tied contact (connection=>contact).
Go to the connection table.
Using the View button, add “adhe path” column.
Right-click on the path ID in the table, Edit.
Press “sketch”. This menu allows points on the path to be deleted, moved, etc.

## Slide 52: Adhesive – connection files
Adhesive connections may be written to and read from a connection file.
Delete all connections.
Read the connection file adhesive.xml.

## Slide 53: Spotwelds - lines
Tools=>Connections=>Lines
Select Spotwelds
Primer automatically finds lines of spotwelds that connect the same panels
2-layer welds
3-layer welds

## Slide 54: Spotwelds - lines
Change pitch of welds
This can also be done using batch commands for incorporation in automatic processes

## Slide 55: Spotwelds - lines
Add adhesive or change spotwelds into adhesive or vice-versa.

## Slide 56: Spotwelds - lines
Re-project lines of MIG welds to follow new mesh/free-edge.

## Slide 57
Training course
Oasys PRIMER: Spotwelding and Connections