## Slide 1: Professor Peter Debney
Making Good Structural Analysis Models
Formed in 1976 to develop software for Arup
Due to success – the software was commercialised with Oasys Ltd incorporated in 1979
Lead developers are engineers who have moved to programming
This presentation is protected by international copyright laws. Reproduction and distribution of the presentation without written permission from Peter Debney or Oasys Ltd is prohibited. Enquiries: oasys@arup.com

## Slide 2: Introduction
Making Good Structural Analysis Models
Nigel Rees
Commercial Manager
Peter Debney
Application Specialist
Visiting Professor Bradford University
The webinar has now started – please check your audio

## Slide 3: Principles of Good Modelling

## Slide 4: As Accurate as is necessary
“It’s better to be roughly right than precisely wrong.” John Maynard Keynes

## Slide 5: As Accurate as is necessary
“Everything is vague to a degree you do not realise until you have tried to make it precise…” Bertrand Russell

## Slide 6: Accuracy - Verification
“the process of determining that a calculation method implementation accurately represents the developer’s conceptual description of the calculation method and the solution of the calculation method.” (ISO 16730)
In other words: is the model correct?

## Slide 7: Accuracy - Verification
Are all the loads, dimensions, sections, and materials correct

## Slide 8: Accuracy - Verification
Are all the loads, dimensions, sections, and materials correct?
Sum total loads and reactions

## Slide 9: Accuracy - Verification
Are all the loads, dimensions, sections, and materials correct?
Sum total loads and reactions
Check mesh shapes are not too stretched

## Slide 10: Accuracy - Verification
Are all the loads, dimensions, sections, and materials correct?
Sum total loads and reactions
Check mesh shapes are not too stretched
Check for very short or long elements

## Slide 11: Accuracy - Verification
Are all the loads, dimensions, sections, and materials correct?
Sum total loads and reactions
Check mesh shapes are not too stretched
Check for very short or long elements
Stability Analysis

## Slide 12: As Realistic as is appropriate
“It is the mark of an educated man to look for precision in each class of things just so far as the nature of the subject admits.” Aristotle

## Slide 13: As Realistic as is appropriate
“Models are simplified reproductions of portions of reality that, if validated, are still able to capture a few of its essential properties.”
Guido Fioretti

## Slide 14: Model Validation
“the process of determining the degree to which a calculation method is an accurate representation of the real world from the perspective of the intended uses of the calculation method.” (ISO 16730)
In other words: is the model realistic?

## Slide 15: Realistic Boundary Conditions

## Slide 16: Realistic Boundary Conditions

## Slide 17: Realistic Restraint Stiffness

## Slide 18: As Simple as possible
"Perfection is achieved not when there is nothing more to add, But when there is nothing left to take away" Antoine de Saint-Exupery

## Slide 19: As Simple as possible
"Make things as simple as possible, but no simpler."
Albert Einstein
Have you included what you need to include?
Have you removed what you can remove?

## Slide 20: Captures the Important behaviours
“All models are approximations. Essentially, all models are wrong, but some are useful. However, the approximate nature of the model must always be born in mind.” George E.P Box and Norman Draper

## Slide 21: Sleipner A Oilrig Collapse

## Slide 22: Checklist for Checking
Stage 1 – look and think
  Is the displaced shape correct?
  Does the bending moments or stress distribution look sensible?
  Are there any discontinuities in the results?
Stage 2 – see if the answers are sensible
  Do a separate hand calculation
  Build a simplified FEA model of the structure
Stage 3 – check really carefully
  Build the model again in another program, or get someone else to do it

## Slide 23: Structural Types Model Types

## Slide 24: Model Types
1D – single beam, column, or slab
2D – portal frame, truss, or floor
3D – whole building or bridge

## Slide 25: 1D Models
Beams
Columns
…

## Slide 26: 2D Models
Plane frame

## Slide 27: 2D models restrain out of plane, but does the design?
Notes: Watch out for out-of-plane effects, whether stability or dynamic

## Slide 28: 2D Models
Plane frame
Floor

## Slide 29: 2D Models
Plane frame
Floor
Plane Stress

## Slide 30: 2D Models
Plane frame
Floor
Plane Stress
Plane Strain

## Slide 31: 2D Models
Plane frame
Floor
Plane Stress
Plane Strain
Axisymmetric

## Slide 32: 3D Models

## Slide 33: Structural Types
Stick
Shell
Mass
1D elements
2D elements
3D elements

## Slide 34: Element Types

## Slide 35: 3D Elements
TET4
BRICK8
/ HEX8
3D Element Formulations
Solid
Infinite
PENT6
Notes: Tetrahedron
Hexahedron / Brick
Pentahedron / Prismatic

## Slide 36: 2D Elements
Linear
Parabolic
QUAD
TRI
TRI3
TRI6
QUAD4
QUAD8
2D Element Formulations
Plane Stress
Plane Strain
Axisymmetric
Plate
Shell
Curved Shell
Fabric
Load Panel
Wall

## Slide 37: 2D Elements – Grid Loads vs. Load Panels

## Slide 38: 2D Elements – Wall Elements

## Slide 39: 1D Elements
1D Element Formulations
Beam
Bar (Truss)
Rod
Strut
Tie
Cable
Spring
Link

## Slide 40: 1D Elements – Ties vs. Sliding Cables

## Slide 41: 0D Elements
0D Element Formulations
Mass
Ground Spring
Notes: Mass elements – dynamic models (or use Loads converted to mass)
Ground Springs – nonlinear boundary conditions

## Slide 42: Conclusion

## Slide 43: What makes a good model?
Good models:
Are as accurate as necessary
Are as realistic as appropriate
Are as simple as possible
Capture the important behaviours

## Slide 44
Peter.Debney@arup.com
www.linkedin.com/in/peterdebney
Notes: Now does anyone have any questions? Just write them in the question box in your control panel